## Slide 1
제품 설계/조립도
<Upper module>
4 x M2.5-5mm
4 x M2.5-5mm
2 x M2.5-5mm
2 x M2-5mm
2 x M2.5-5mm
2 x M2-5mm
Upper cover
Raspberry camera module
Husky camera
Power switch
C type charging port
2 x M2.5-5mm
2 x M2.5-5mm
2 x M2.5-5mm
2 x M2.5-5mm
2 x M2.5-5mm
Lower cover
Botton cover
Dot module`
Select button
7.4v Li-Po battery
2 x 5V step down module
vibration module
<Lower module>

## Slide 2
제품 설계/조립도
Weight | 1.2kg (including cane) | 
Dimensions | Total | 150 x 380 x 80mm
 | folded | 150 x 1250 x 80mm
Service | 1. Traffic light recognition | 
 | 2. Currency recognition 3. IoT - Face recognition - Home appliance control | 
Actuation | Dot feedback haptic feedback | 
Electronics | Raspberry Pi 4 7.4v Li-Po battery 2200mAh 5V USB C type charging | 
<개발된 디바이스>

## Slide 3
제품 설계/조립도
 | 품명 | 품번 | 수량 | 비고
1 | Upper cover | - | 1 | 3D 프린팅
2 | Lower cover | - | 1 | 3D 프린팅
3 | Bottom cover | - | 1 | 3D 프린팅
4 | Power switch | HX12-A5 | 1 | 
5 | C type charging module | HAM5005 | 1 | 
6 | Raspberry camera module | - | 1 | 
7 | Husky camera | - | 1 | 
8 | vibration module | ICF1383 | 1 | 
 | 품명 | 품번 | 수량 | 비고
9 | Select button | HX12-C4 | 4 | 
10 | 5V step down module |  | 2 | https://smartstore.naver.com/zxmas1005/products/5666703065?NaPm=ct%3Dl7fkqljc%7Cci%3Dcheckout%7Ctr%3Dppc%7Ctrx%3D%7Chk%3Daa0e235eecaabf0e054f6a0801d486bfff9ea62f
11 | 7.4v Li-Po battery |  | 1 | 
12 | Dot module |  | 1 | 
13 | M2.5 bolt 5mm |  | 22 | 
14 | M2 bolt 5mm |  | 6 | 
15 | Cane |  | 1 | https://smartstore.naver.com/momo2000/products/4858337603?NaPm=ct%3Dl7fkq4li%7Cci%3Dcheckout%7Ctr%3Dppc%7Ctrx%3D%7Chk%3D4dac3cc09b777cc672391d91d16e9181d3349e4e